Operation attention for the Boming laser equipment

1. Switch on the general power, then switch on the laser power when starting machine; Switch off the laser power, then switch off the general power when stopping the machine.

2.After machine starting, check if the inlet and outlet water in chiller can flow freely; the seller isn’t responsible for the breaking of laser tube due to no water flowing.

3.Change the water in chiller every two months, use purified water. The water temperature isn’t over 35℃。

4. Clean the lens once a day, don't start the machine within 2min after cleaning. The seller isn’t responsible for the breaking of lens due to water on them after cleaning.

5. Clean the air blower once a week.

6. It is not allowed to put hands inside the working area when machine working, the persons are at their own risk if breaching the rule.

7. The worker need to watch the machine when working. The seller isn’t responsible for fire broke out without people watching.